Quotation Call Notice

Sealed quotations are invited from registered Firms/Agencies having valid VAT/TIN/PAN/Registration documents for supplying 16 Nos. of 15 meter SC to LC Single mode fiber patch cable with laying Accessories for CCL-1 as per specification given below:

Item with Specification, Quantity

1:- SC-LC Single Mode OFC Patch Cords 9/125 Micron:- Type of connectors-SC or LC LSOH Jacket - Reduces toxic / corrosive, Length-15 meters, Polishing-100% Factory polished and tested Insertion Loss-Less than 0.35dB per connector,  Attenuation-0.4dB/km over 1310nm to 1625nm, Standards-ROHS Compliant, Jacket colour-Industry Standard Colour - OS1-Yellow,OM3-Aqua,OM2-Grey,OM1-Orange,Make and Type-SC to LC Duplex Fiber Optic Patch Cord 9/125 Micron, Cable Sheath-LSZH, Cable Diameter-1.6 mm, Ferrule-Ceramic, Buffer-Tight buffered, Temperature Range-.-40 Degree C to +85 Degree C Buffer Diameter:-900μm, Primary Coating-245μm, Strength Member:-Aramid Yarn, Jacket Material:-LS0H IEC 61034-1 & 2, IEC-60332-1, IEC-60754- 1 & 2

2:- laying Accessories:- 15meter PVC 4"  Casing Capping with 100 Nos. grip and 100Nos. Steel Screw.(2”)

The cost of the above mentioned items should be quoted mentioning make and detailed technical specification. The intenders are required to submit the offer along with the VAT/TIN/PAN/Registration certificates. The Firms/Agencies should write quotations for “16 Nos. of 15 meter SC to LC Single mode fiber patch cable with laying Accessories for CCL-1” in bold letters on covered envelope. The firm should not be black listed during last three financial years.

The last date submission of quotations is 23/07/2016 up to 4.00 PM addressing to the Principal, College of Engineering and Technology, Techno Campus, Mahalaxmivihar, Ghatikia, Bhubaneswar-29 by Speed post/Registered post/Courier only. The authority will not be responsible for any postal delay. No hand delivery will be accepted.

The authority reserves the right to reject any or all quotations without assigning any reason thereof.

Sd/-

PRINCIPAL

Copy to- HOD CSE for information and necessary action