Quotation Call Notice

Sealed quotations are invited from registered Firms/Agencies having valid VAT/TIN/PAN/Registration documents to supply and install the following items for Boys Hostel RHR, CET campus, CET, BBSR as specified below:

Item with Specification						Quantity

- 8- Chanel HD CVI DVR					01

Warranty: - 1 Year

- 1.3 Megapixel HD CVI IR Doom Camera(20mtr)			04

Warranty: -  1 Year

- 1.3 Megapixel HD CVI IR Bullet Camera(60mtr)			01

Warranty: -  1 Year

- 1 TB Hard disk(HDD), Warranty: -  1 Year			01

- 24”LED Display						01

Warranty: - 3Years

- VNC Pin, Warranty: -  1 Year					10

- DC Connector, Warranty: -  1 Year				05

- 10 Amp power supply, Warranty: -  1 Year			01

- Casing capping with copper cable per meter

with one year warranty				as per actual

8-Chanel HD CVI DVR: - Support HDCVI/Analog/IP Video input, All channel 720P Realtime Recording, H.264 dual-stream Video Compression, HDMI / VGA / TV Simultaneous Video Output, Support Multi-brand network cameras,  Support 1 SATA HDDs up to 8TB, 2 USB2.0, Mobile Software with CMS Software, Embedded processor, 1920x1080, 1280x1024, 1280x720, 1024x768 Video Resolution, 1 HDMI, 1 VGA, 1 TV Video output, Main Stream: 720P/960H / D1(1-25/30fps), Extra Stream: CIF / QCIF(1-25/30fps) video recording, 1/4/8/9/16/25/36 Video Display Split, Manual, Schedule(Regular(Continuous), MD), Stop in Recording Mode, Play, Pause, Stop, Rewind, Fast play, Slow play, Next file, Previous file,Next camera, Previous camera, Full screen, Repeat, Shuffle, Backup, selection, Digital zoom in Playback, RJ-45 port (10/100M/1000M) for Ethernet.

1.3 Megapixel HD CVI IR Doom Camer(20mtr):- 1/2.9" 1.3MP HQIS Pro Image Sensor, 25/30fps@1.3MP, Day/Night(ICR), AWB, AGC, BLC,  3.6mm Lens, IR Range of 20 Mtr, S/N ratio>50db, 1.3MP @25fps for video streaming, 24Nos. of IR LEDs.

1.3 Megapixel HD CVI IR Bullet Camera(60mtr):- 1/2.9" 1.3MP HQIS Pro Image Sensor, 25/30fps @1.3MP, Day/Night(ICR), AWB, AGC, BLC, 12mm Lens, IR Range of 60 Mtr., IP66, 1/60-1/100,000sec shutter speed, 12mm lens>50db s/n ratio, 1.3mp@25fps for video streaming, 1.0vp-p75 for video output, 195mm x 125mm x 110mm in dimension, 4 pcs array for IR LEDs.

1 TB Hard disk(HDD):- Seagate, Samsung, Fujistu, Hitachi, Sony. Copper VNC Pin.

24”  LED Display Make: Samsung/LG/Sony/Phillips (with 3 years warranty)

The cost of the above mentioned item should be quoted mentioning make, model number and detailed technical specification. The intenders are required to submit the offer along with the VAT/TIN/PAN/Registration certificates. The Firms/Agencies should write quotations for “Supply and installation of CCTV cameras for Boys Hostel RHR, CET, Bhubaneswar” in bold letters on covered envelops. The firm should not be black listed during last three financial years.

The last date submission of quotations is ______________ before 3.00 PM addressing to the Principal, College of Engineering and Technology, Techno Campus, Mahalaxmi vihar, Ghatikia, Bhubaneswar-29 by Speed post/Registered post/Courier only. No hand delivery is accepted. The authority will not responsible for any postal delay.

The authority reserves the right to reject any or all quotations without assigning any reason thereof.

Sd/-

Principal